## Slide 1: 3D Photography
Sensors

## Slide 2: Perspective projection

## Slide 3: Pinhole & the Perspective Projection
SCREEN
SCENE
(x,y)
Is there an image being formed on the screen?

## Slide 4: Pinhole Camera
Pinhole
Object
Pinhole camera
“Camera obscura” – known since antiquity
Image
Image plane

## Slide 5: Perspective Camera
(X,Y,Z)
(x,y,z)
Center of
Projection
r
r’
r =[x,y,z]T
r’=[X,Y,Z]T
r/f=r’/Z
f: effective focal length:
distance of image plane from O.
x=f * X/Z
y=f * Y/Z
z=f
From Trucco & Verri

## Slide 6: Magnification
(X,Y,Z)
(x,y)
Center of
Projection
(X+dX,Y+dY,Z)
(x+dx,y+dy)
x/f=X/Z
y/f=Y/Z
(x+dx)/f=(X+dX)/Z
(y+dy)/z=(Y+dY)/Z
dx/f=dX/Z
dy/f=dY/Z
=>
d
d’
From Trucco & Verri

## Slide 7: Magnification
(X,Y,Z)
(x,y)
Center of
Projection
(X+dX,Y+dY,Z)
(x+dx,y+dy)
d
d’
Magnification: |m|=||d’||/||d||=|f/Z|
or m=f/Z
m is negative when image is inverted…
From Trucco & Verri

## Slide 8: Implications For Perception*
* A Cartoon Epistemology: http://cns-alumni.bu.edu/~slehar/cartoonepist/cartoonepist.html
Same size things get smaller, we hardly notice…
Parallel lines meet at a point…

## Slide 9: Vanishing Points
(from NALWA)

## Slide 10: Vanishing points
VPL
VPR
H
VP1
VP2
VP3
Different directions correspond
to different vanishing points
Marc Pollefeys

## Slide 11: 3D is different…

## Slide 12: 3D Data Types: Volumetric Data
Regularly-spaced grid in (x,y,z): “voxels”
For each grid cell, store
  Occupancy (binary: occupied / empty)
  Density
  Other properties
Popular in medical imaging
  CAT scans
  MRI

## Slide 13: Voxelized example

## Slide 14: 3D Data Types: Surface Data
Polyhedral
  Piecewise planar
  Polygons connected together
  Most popular: “triangle meshes”
Smooth
  Higher-order (quadratic, cubic, etc.) curves
  Bézier patches, splines, NURBS, subdivision surfaces, etc.

## Slide 15: Example of triangle mesh

## Slide 16: 2½-D Data
Image: stores an intensity / color along each of a set of regularly-spaced rays in space
Range image: stores a depth along each of a set of regularly-spaced rays in space
Not a complete 3D description: does not store objects occluded (from some viewpoint)
View-dependent scene description

## Slide 17: 2½-D Data
This is what most sensors / algorithms really return
Advantages
  Uniform parameterization
  Adjacency / connectivity information
Disadvantages
  Does not represent entire object
  View dependent

## Slide 18: 2½-D Data
Range images
Range surfaces
Depth images
Depth maps
Height fields
2½-D images
Surface profiles
xyz maps
…

## Slide 19: Example of range image

## Slide 20: Point Clouds
A collection of 3D points
Order does not matter
Usually the concatenation of various range images

## Slide 21: Example point clouds

## Slide 22: Example of point clouds

## Slide 23: Range Acquisition Taxonomy
Range acquisition
Contact
Transmissive
Reflective
Non-optical
Optical
Industrial CT
Mechanical (CMM, jointed arm)
Radar
Sonar
Ultrasound
MRI
Ultrasonic trackers
Magnetic trackers
Inertial (gyroscope, accelerometer)

## Slide 24: Range Acquisition Taxonomy
Optical methods
Passive
Active
Shape from X:
stereo
motion
shading
texture
focus
defocus
Active variants of passive methods
Stereo w. projected texture
Active depth from defocus
Photometric stereo
Time of flight
Triangulation

## Slide 25: Optical Range Acquisition Methods
Advantages:
  Non-contact
  Safe
  Usually inexpensive
  Usually fast
Disadvantages:
  Sensitive to transparency
  Confused by specularity and interreflection
  Texture (helps some methods, hurts others)

## Slide 26: Stereo
Find feature in one image, search along epipolar line in other image for correspondence

## Slide 27: Stereo Vision
depth map

## Slide 28: Triangulation
f
T
Z
P
pl
pr
Ol
Or
Left Camera
Right Camera
X-axis
Z-axis
cl
cr
Fixation
Point:Infinity.
Parallel
optical axes.
Calibrated Cameras
Similar triangles:
d:disparity (difference in retinal positions).
T:baseline.
Depth (Z) is inversely proportional to d (fixation at infinity)

## Slide 29: Traditional Stereo
Inherent problems of stereo:
    Need textured surfaces
    Matching problem
    Baseline trade-off
    Unstructured point set
However
  Cheap (price, weight, size)
  Mobile
  Depth plus Color
Sparse estimates
Unreliable results

## Slide 30: Why More Than 2 Views?
Baseline
  Too short – low accuracy
  Too long – matching becomes hard

## Slide 31: Multibaseline Stereo
[Okutami & Kanade]

## Slide 32: Shape from Motion
“Limiting case” of multibaseline stereo
Track a feature in a video sequence
For n frames and f features, have 2nf knowns, 6n+3f unknowns

## Slide 33: Photometric Stereo Setup
[Rushmeier et al., 1997]

## Slide 34: Photometric Stereo
Use multiple light sources to resolve ambiguity
In surface orientation.
Note: Scene does not move – Correspondence
between points in different images is easy!
Notation: Direction of source i: or
Image intensity produced by source i:

## Slide 35: Lambertian Surfaces (special case)
orientation
albedo
Use THREE sources in directions
Image Intensities measured at point (x,y):

## Slide 36: Photometric Stereo: RESULT
orientation
albedo
INPUT

## Slide 37: Data Acquisition Example
Color Image of Thomas Hunter
Building, New York City.
Range Image of same
building. One million 3D points.
Pseudocolor corresponds to laser
intensity.

## Slide 38: Time-of-flight scanners
Also known as LIDAR
Light Detection And Ranging

## Slide 39
Data
Acquisition
Spot laser scanner.
Time of flight.
Max Range: 100 meters.
Scanning time: 16 minutes
for one million points.
Accuracy: ~6mm per range point

## Slide 40
Data
Acquisition
Leica ScanStation 2
Spherical field of view.
Registered color camera.
Max Range: 300 meters.
Scanning time: 2-3 times faster
Accuracy: ~5mm per range point

## Slide 41: Data Acquisition, Leica Scan Station 2, Park Avenue and 70th Street, NY

## Slide 42: Cyclone view and Cyrax Video

## Slide 43: Pulsed Time of Flight
Send out pulse of light (usually laser), time how long it takes to return

## Slide 44: Pulsed Time of Flight
Advantages:
  Large working volume (more than 100 m.)
Disadvantages:
  Not-so-great accuracy (at best ~5 mm.)
    Requires getting timing to ~30 picoseconds
    Does not scale with working volume
Often used for scanning buildings, rooms, archeological sites, etc.

## Slide 45: Data Acquisition, Leica Scan Station 2, Park Avenue and 70th Street, NY

## Slide 46: Video

## Slide 47: Other range sensors (some based on PrimeSense/Kinect)
Matterport
DotProduct
Google Project
Tango Prototype

## Slide 48: Real-time range sensors == self driving cars

## Slide 49: Open datasets
KITTI <self driving> http://www.cvlibs.net/datasets/kitti/
Waymo (just announced) <self driving>
https://waymo.com/open/
SunRGBD <indoor>
http://rgbd.cs.princeton.edu/

## Slide 50
Park Avenue: Six registered scans (top view)

## Slide 51
3D PHOTOGRAPHY EXAMPLE
Ten scans were acquired of façade of
Thomas Hunter Building (NYC)
Registration details
Automatic registration.
Each scan has a different color.

## Slide 52
3D PHOTOGRAPHY EXAMPLE
24 scans were acquired of façade of
Shepard Hall (City College of NY)

## Slide 53: TEXTURE MAP ANIMATION

## Slide 54: Optical Triangulation
Lens
Sheet of
light
CCD array
Sources of error:
1) grazing angle,
2) object boundaries.

## Slide 55
Optical Triangulation
Lens
Sheet of
light
CCD array
Sources of error:
1) grazing angle,
2) object boundaries.

## Slide 56: Active Optical Triangulation
Xc
Yc
Zc
Image
Light Stripe System.
Light Plane:
AX+BY+CZ+D=0
(in camera frame)
Image Point:
x=f X/Z, y=f Y/Z
(perspective)
Triangulation: Z=-D f/(A x + B y + C f)
Move light stripe or object.

## Slide 57: Triangulation

## Slide 58: Triangulation: Moving the Camera and Illumination
Moving independently leads to problems with focus, resolution
Most scanners mount camera and light source rigidly, move them as a unit

## Slide 59: Triangulation: Moving the Camera and Illumination

## Slide 60: Triangulation: Moving the Camera and Illumination

## Slide 61: The Digital Michelangelo Project

## Slide 62: Marc Levoy (Stanford)
calibrated motions
  pitch (yellow)
  pan (blue)
  horizontal translation (orange)
uncalibrated motions
  vertical translation
  remounting the scan head
  moving the entire gantry

## Slide 63: Scanner design
4 motorized axes
laser, range camera,
white light, and color camera
truss extensions
for tall statues
Notes: 0:30

## Slide 64: Scanning the David
height of gantry: 7.5 meters
weight of gantry: 800 kilograms
Notes: 2:30 through closeup of eye
0:40
So here we are scanning our “piece de resistance”
  the gantry is extended to nearly its full height
If you’ve looked at our web site
  you know the little story about the gantry being too short initially
  because we relied on art history books for the height of the David
  and they're all wrong – by 3 feet !!
  so at the last minute we had to add a piece to the gantry…here
  and load another few hundred pounds of ballast to the base…here – to keep the gantry from tipping over on the statue
But as you can see from the photo on the right,
  we did finally reach the top of the statue
0:45
4:00 through architectural reps

## Slide 65: Triangulation Scanner Issues
Accuracy proportional to working volume (typical is ~1000:1)
Scales down to small working volume (e.g. 5 cm. working volume, 50 m. accuracy)
Does not scale up (baseline too large…)
Two-line-of-sight problem (shadowing from either camera or laser)
Triangulation angle: non-uniform resolution if too small, shadowing if too big (useful range: 15-30)

## Slide 66: Triangulation Scanner Issues
Accuracy proportional to working volume (typical is ~1000:1)
Scales down to small working volume (e.g. 5 cm. working volume, 50 m. accuracy)
Does not scale up (baseline too large…)
Two-line-of-sight problem (shadowing from either camera or laser)
Triangulation angle: non-uniform resolution if too small, shadowing if too big (useful range: 15-30)

## Slide 67: Multi-Stripe Triangulation
To go faster, project multiple stripes
But which stripe is which?
Answer #1: assume surface continuity

## Slide 68: Multi-Stripe Triangulation
To go faster, project multiple stripes
But which stripe is which?
Answer #2: colored stripes (or dots)

## Slide 69: Multi-Stripe Triangulation
To go faster, project multiple stripes
But which stripe is which?
Answer #3: time-coded stripes

## Slide 70: Time-Coded Light Patterns
Assign each stripe a unique illumination code over time [Posdamer 82]
Space
Time

## Slide 71: Laser-based Sensing
Provides solutions
  Dense & reliable
  Regular grid
But
  Complex & large point sets
  Redundant point sets
  No color information (explain this)
  Expensive, non-mobile
Adjacency info
Mesh

## Slide 72: Major Issues
Registration of point sets
Global and coherent geometry
  remove redundancy
  handle holes
  handle all types of geometries
Handle complexity
  Fast Rendering

## Slide 73: Representations of 3D Scenes
Geometry and Material
Geometry and Images
Images with Depth
Colored Voxels
Light-Field/Lumigraph
Panorama with Depth
Complete description
Traditional texture mapping
Scene as a light source
Global
Geometry
Local
Geometry
False
Geometry
Panorama
No/Approx.
Geometry
Facade

## Slide 74: Head of Michelangelo’s David
photograph
1.0 mm computer model
Notes: 0:20
We haven’t assembled the David at full-resolution yet
Here’s a 1 mm model of the head
  watertight
  with color
The photograph at the left was taken with uncalibrated lighting
  so the two images don’t match exactly
  but hopefully you agree that we’ve basically captured the statue’s appearance

## Slide 75: David’s left eye
holes from Michelangelo’s drill
artifacts from space carving
noise from laser scatter
0.25 mm model
photograph
Notes: 0:30
Here’s a closeup of David’s left eye
  at the maximum resolution of our model – ¼ mm
  we can see some interesting things…
These bumps
  are holes from Michelangelo’s drill
  so that’s real geometry
These bumps
  are artifacts from space carving, the hole-filling part of our range image merging algorithm
  smoothing out those artifacts, while preserving the observed surfaces, is future work
Finally, these bumps
  are noise from laser subsurface scattering
Let’s zoom in some more
  and look at the triangle mesh
0:45

## Slide 76: IBM’s Pietà Project
Michelangelo’s “Florentine Pietà”
Late work (1550s)
Partially destroyed by Michelangelo, recreated by his student
Currently in the Museo dell’Opera del Duomo in Florence

## Slide 77: Scanner
Visual Interface “Virtuoso”
Active multibaseline stereo
Projector (stripe pattern), 6 B&W cameras, 1 color camera
Augmented with 5 extra “point” light sources for photometric stereo (active shape from shading)

## Slide 78: Data
Range data has 2 mm spacing, 0.1mm noise
Each range image: 10,000 points, 2020 cm
Color data: 5 images with controlled lighting, 1280960, 0.5 mm resolution
Total of 770 scans, 7.2 million points

## Slide 79: Scanning
Final scan June 1998, completed July 1999
Total scanning time: 90 hours over 14 days (includes equipment setup time)

## Slide 80: Results

## Slide 81: HUNTER COLLEGE (our work):
Segmented Planar Area.
Exterior and Interior borders shown.
Interior
border.
Range sensing
direction.
Each Segmented
Planar Area is
shown with different
color for clarity.
Exterior border.
Intersection
line.

## Slide 82: HUNTER COLLEGE

## Slide 83: HUNTER COLLEGE: Final result – 24 scan pairs ~600 lines per scan

## Slide 84: HUNTER COLLEGE: Matching 3D with 2D imagery
3D parallelepipeds
2D rectangles
Matches shown in blue

## Slide 85: HUNTER COLLEGE: Virtual (synthetic) scene views

## Slide 86: Virtual (synthetic) scene views

## Slide 87: Virtual (synthetic) scene views